## Slide 1
www.cyi.ac.cy
Routine UAV atmospheric observations:
Are we ready for that ?
J. Sciare et al.
Contribution for JRA1 – ACTRIS2

## Slide 2
Motivations
  In the near future Atmospheric instrument will become smaller and cheaper offering new field of applications
  The use of Unmanned Aerial Vehicle (UAV) offers new potential for atmospheric observations
  What is the added value for the ground-based ACTRIS network ?
  How mature are these new atmospheric sensors for ACTRIS ? (data quality)
  How easily these techniques can be disseminated to end-users ?
  How mature are these new technical developments for routine operation in the ACTRIS network ? (monitoring capacity)

## Slide 3
  Cyprus – CAO station
  2016-2017
Strategy
  Establish a UAV research infrastructure that has a the capacity to integrate miniaturized instrumentation and fly them
  Operate routine (weekly) flights for a period of 1 years and learn from this experience
  To evaluate the real added value compared to ground-based in-situ observations

## Slide 4
Latitude :35°02′18″N
Longitude :33°03′38″E
Altitude : 550m asl
Cyprus Atmospheric Observatory
December 2014
March 2015
April 2016
100 access days for users
  EU-H2020 ACTRIS2 Trans-national Access
LSCE
MD
LaMP
CNRS-GAME
LA
LOA

## Slide 5: Unmanned System Research Laboratory (USRL)
  100 m2 Laboratory (workshop facilities, 3D printing, …) equipped for unmanned systems research & development
  Next to the CyI Instrumentation & Chemistry laboratories for atmospheric sciences
http://www.cyi.ac.cy/index.php/usrl.html
  Hands-on training in our accredited Ph-D on Atmospheric Sciences
  New lab facilities (Est. since 2014)

## Slide 6
http://www.cyi.ac.cy/index.php/usrl.html
Unmanned System Research Laboratory (USRL)
  Two professional pilots (flying on commercial companies – Airbus family)
  → Unparalleled knowledge on safety procedures and flight operations in liaison with the Civil Aviation Authorities
  Two electronic engineers
  → Design, optimization and realization of the Unmanned Systems’ wiring, maintenance and enhancement of the electronic components, Research and integration of new technologically advanced and innovative electronic components on the UAVs
  Two mechanical engineers
  → Designing/Operating 2d and 3d drawings using computer-aided modelling software& manufacturing machines for prototyping, UAV construction/maintenance of parts using various material
  Two post-doctoral fellows in experimental atmospheric sciences
  → Operating, calibrating, processing data from miniaturized instruments running onboard UAV

## Slide 7: Mobile Ground Control Station (GCS)
Truck with GCS
Portable GCS
Monitoring & Control of UAV, Payload, Camera
Monitoring & Control of UAV, Payload, Camera
http://www.cyi.ac.cy/index.php/usrl.html
Unmanned System Research Laboratory (USRL)

## Slide 8: Fleet of Unmanned Aerial Vehicles (UAVs)
  Fixed Wing
  Rotary Wing
Medium Size: 35 Kg Weight Payload: 12 Kg Endurance: up to 4 hours Ceiling: up to 4 Km
  4 platforms
Small Size: 10 Kg Weight Payload: 4 Kg Endurance: ~30 min Ceiling: up to 2 Km
  1 platform
Small Size: 9 Kg Weight Payload: 2 Kg Endurance: ~20 mins Ceiling: up to 1 Km
  1 platform
http://www.cyi.ac.cy/index.php/usrl.html
Unmanned System Research Laboratory (USRL)
  4 platforms
Small Size: 5 Kg Weight Payload: 2 Kg
Endurance: up to 2 hours Ceiling: up to 4 Km

## Slide 9
Private UAV runway and Airspace facility
  Private Runway (CyI)
  Flat Terrain Remote Area
  25 Km West of Nicosia
  Exclusive Overhead Airspace committed for CyI UAVs up to 3km asl
  Located 4 Km from CyI ground-based Atmospheric Observatory (Agia Marina)
http://www.cyi.ac.cy/index.php/usrl.html
Unmanned System Research Laboratory (USRL)

## Slide 10
Unmanned Aerial Instrumentation
MetOne Optical Particle Counter (OPC)
Printed Optical Particle Spectrometer (POPS)
AEROSOL SIZE DISTRIBUTION
Ice Nuclei (IN) single & multi-Sampler prototype: University of Frankfurt
ICE NUCLEI SAMPLER
  Dual Wavelength Prototype (DWP) Aethalometer prototype: Aerosol d.o.o.,Slovenia
  μ-aethalometer
ABSORPTION
AEROSOL OPTICAL DEPTH
http://www.cyi.ac.cy/index.php/usrl.html
Unmanned System Research Laboratory (USRL)
T – RH
On-Screen-Display Video
Autopilot - ADC
UAV - BASIC

## Slide 11
Integration & in-flight qualification
http://www.cyi.ac.cy/index.php/usrl.html
Unmanned System Research Laboratory (USRL)
  Integration of instrumentation to match UAV payload, size constrains, weight balance
  Interference with UAV control systems
  In-flight conditions (P, T, RH) on instrumentation performance
  Weather simulation chamber (P, T, RH)

## Slide 12
Field campaigns (2016)
INUIT - BACCHUS-ACTRIS
(April 2016)
UAV team
Agia Marina Xyliatou team
Remote sensing team
Analytical lab team
Limassol
Nicosia
Agia Marina
Xyliatou
  A total of 50 flights within a period of 3 weeks with up to 3-4 profiles (0-3km asl) during dust episods

## Slide 13
BC
Investigating the atmospheric column:
Synergy between remote sensing (Lidar) and in-situ (UAV)
boundary
layer
INUIT – BACCHUS - ACTRIS
Cyprus ( April 2016)

## Slide 14
Troodos station
(1880m asl)
Agia Marina Xiliatou Station
(500 m asl)
350-3,000 m asl
boundary layer
Free troposphere
1000-1500m
UAV
Payload = DWP, T, RH, video
Payload = IN sampler, T, RH
Payload = miniSASP, POPs, OPC (MetOne)
Payload = to be defined (2kg)
Flight Strategy – 1 day flight / week / Focus on contrasted situations
- Clean (Med.) vs Polluted (Europe/Turkey/Middle East)
- Dust (Africa) vs Dust (Middle East)
- Aerosol layer (boundary layer) vs aerosol layer (Free troposphere)
- Aircraft campaigns (March-April 2017)
UAV monitoring activities : Experimental setting
(July 2016 – July 2017)

## Slide 15
350-3,000 m asl
boundary layer
Free troposphere
1000-1500m
UAV
PM2.5 (POPs)
O3
BC
OPC
Sunphotomer (MiniSASP)
Agia Marina Xyliatou Station
(500 m asl)
PM2.5
O3
BC
OPC
Sunphotomer
Agia Marina Xyliatou Station
(550 m asl)
Troodos station
(1900m asl)
O3
BC
OPC
Troodos Station
(1,900 m asl)
UAV
(350- 3,000 m asl)
  Multi-level comparison of key parameters

## Slide 16
Conclusions & Perspectives
  This UAV atmospheric monitoring program will be used as a “proof of concept” to evaluate to 1) its real added value compared to ground-based (in-situ + remote sensing) observations, 2) its potential for replicability and dissemination, 3) its real operating cost
  Several communities may be interested in atmospheric UAV tools (EUFAR, ACTRIS, ICOS, …). We need to identify in which community such tools would better fit
  We have also to explore what are the needs from end-users (services, training, easy-to-use integrated tool, …) and evaluate if they can be afforded and at which cost